## Slide 1: Time-Frequency Analysis
Ram Bilas Pachori
Discipline of Electrical Engineering
Indian Institute of Technology Indore

## Slide 2: Overview
Transform
Fourier Transform (FT)
Short Time Fourier Transform (STFT)
Continuous Wavelet Transform (CWT)
Discrete Wavelet Transform (DWT)
Wigner-Ville Distribution (WVD)
Hilbert-Huang Transform (HHT)
Conclusion

## Slide 3: Transform
Transform: A mathematical operation that takes a function or sequence (one domain) and maps it into another one (other domain)
We need signal transforms because
  The transform provides hidden information about the original function or signal
  The transform helps to solve a differential equation
  The transform may provide data compression and storage may require less memory
  Some operations may be easier to apply in the transform domain (Example: Convolution operation in LTI systems).

## Slide 4: Fourier Representation (December, 21, 1807)
Jean B. Joseph Fourier
(1768-1830)
“An arbitrary function, continuous or with discontinuities, defined in a finite interval by an arbitrarily capricious graph can always be expressed as a sum of sinusoids”
J.B.J. Fourier
Prism

## Slide 5: Fourier’s work
1807, J.B. Fourier:
  All periodic functions can be expressed as a weighted sum of trigonometric functions
  Denied publication by Lagrange, Legendre and Laplace
  1822: Fourier’s work was finally published
  …
  …
  1965, Cooley & Tukey: Fast Fourier Transform
143 years

## Slide 6: Fourier Transform
Complicated signal representation in terms of simple signals
(Basis functions: sinusoidal functions)
Fourier transform is like a bridge between time domain and frequency domain
Analysis and synthesis equations for Fourier transform are as:

## Slide 7: Example
Time domain
Frequency domain

## Slide 8: Shortcomings of the Fourier Transform
Fourier transform identifies all frequency components present in the signal, however it does not provide any information regarding the time localization of these frequency components
Stationary signals consist of frequency components that do not change in time
  all spectral components exist at all times (time information is not required)
  Fourier transform works fine for stationary signals
Non-stationary signals consist of time varying frequency components
  Fourier transform is not suitable for such type of signals
  For such signals, we need to determine time localization of frequency components

## Slide 9: Example
Stationary signal
Nonstationary signal
Frequency domain

## Slide 10
Sinusoids /exponentials basis functions in Fourier transform (global analysis):
  Stretch into infinity in time, therefore has no time localization
  Instantaneous in frequency, therefore has perfect frequency localization
  Need a time dependent frequency representation (or time-frequency representation) for nonstationary signals.
Motivation for Time-Frequency Representation

## Slide 11
STFT of signal x(t):
Computed for each
window centered at t=t’
Time
parameter
Frequency
parameter
Signal to
be analyzed
Windowing
function
Windowing function
centered at t=t’
FT Kernel
(basis function)
Short Time Fourier Transform (STFT)

## Slide 12: Example
t’=-8 t’=-2
t’=4 t’=8

## Slide 13: Spectrogram:
STFT is a complex quantity
STFT is a linear operator
Spectrogram: squared magnitude of STFT
Spectrogram is nonlinear operator
D. Gabor (1946)
Gaussian window
Gabor transform

## Slide 14: Example: Speech signal (MATLAB)
Narrowband spectrogram
(large window, 256 samples)
Wideband spectrogram
(Short window, 64 samples)

## Slide 15: Matlab code
clc;
clear all;
close all;
load mtlb
n=1:4001;
plot(n-1,mtlb)
xlabel('Time index n');
ylabel('Amplitude');
figure;
nfft=input('Type in the window length=');
ovlap=input('Type in the desired overlap=');
specgram(mtlb,nfft,7418,hamming(nfft),ovlap)

## Slide 16: Example: Linear chirp signal
Narrowband spectrogram
(large window, 256 samples)
Wideband spectrogram
(Short window, 128 samples)

## Slide 17: Matlab Code
clc;
clear all;
close all;
t=0:0.001:2;
y=chirp(t,0,1,150);
specgram(y,128,1E3,128,120);

## Slide 18: Shortcoming of STFT
STFT provides the time information by computing a different Fourier transforms of the truncated signal using a sliding window function
How to select type and size of the window? problem!
Wide analysis window provides poor time resolution and good frequency resolution
Narrow analysis window provides good time resolution and poor frequency resolution

## Slide 19: Window Functions
Bartlett window
Blackman window
Bohman window
Chebyschev window
Hamming window
Hanning window
Kaiser window
Rectangular window
Triangular window
Gaussian window
Matlab:
w=window(@hamming,N);

## Slide 20: Heisenberg Principle
Time resolution
How well two spikes in time can be separated from each other in the transform domain
Frequency resolution
How well two spectral components can be separated from each other in the transform domain
Both time and frequency resolutions cannot be high!

## Slide 21: Wavelet
A wavelet is a waveform of limited duration that has an average value of zero.
Comparison of wavelets with sine waves, which are the basis functions of Fourier analysis.
  Sinusoids do not have limited duration — they extend from minus to plus infinity. And where sinusoids are smooth and periodic, wavelets tend to be irregular and a periodic.
Some foods are better handled with a fork than a spoon

## Slide 22: Continuous Wavelet Transform (CWT)
Overcomes the fixed resolution problem of the STFT by using a variable length window
Analysis windows of different lengths are used for different frequencies:
  Narrow window analysis of high frequencies provides good time resolution and poor frequency resolution
  Wide window analysis of low frequencies provides good frequency resolution and poor time resolution
This works well, if the signal to be analyzed mainly consists of slowly varying characteristics with occasional short high frequency bursts

## Slide 23: CWT (Contd…)
Continuous wavelet transform of the signal x(t) using the analysis wavelet (.)
Translation parameter, measure of time
Scale parameter, measure of frequency
The mother wavelet. All kernels are obtained by translating (shifting) and/or scaling the mother wavelet
A normalization
constant
Signal to be analyzed
Scale = 1/frequency

## Slide 24: Example
High frequency (small scale)
Low frequency (large scale)

## Slide 25: Multiresolution Property

## Slide 26: History
Late 1970s, Morlet’s (geophysical engineer) : Windows to be generated from dilation / compression of prototype small, oscillatory signals  wavelets
Criticism for lack of mathematical proof!!!
Early 1980s, Grossman (theoretical physicist): Formalize the transform and devise the inverse transformation  First wavelet transform !
1984-1985, Yeves Meyer: Develop orthogonal wavelet basis functions with better time and frequency localization.
Ingrid Daubechies:
  Discretization of time and scale parameters of the wavelet transform
  Wavelet frames, 1986
  Orthonormal bases of compactly supported wavelets (Daubechies wavelets), 1988

## Slide 27: History
Stephane Mallat:
  Multiresolution analysis w/ Meyer, 1986
  Ph.D. dissertation, 1988
  Discrete wavelet transform
  Cascade algorithm for computing DWT
Martin Vetterli & Jelena Kovacevic
  Wavelets and filter banks, 1986
  Perfect reconstruction of signals using FIR filter banks, 1988
  Sub-band coding
  Multidimensional filter banks, 1992

## Slide 28: Scalogram
Wavelet transform may be a complex quantity
Wavelet transform is a linear operator
Scalogram: squared magnitude of wavelet transform
Scalogram is a nonlinear operator
Cross Terms: when frequencies are very closer

## Slide 29: Scalogram in Matlab
Coefficients = CWT(S,SCALES,'wname',plot)
signal
scale range
name of the wavelet
plot

## Slide 30: Example 1
Time domain
Time-scale domain

## Slide 31: Matlab code
clc;
clear all;
close all;
t = linspace(-1,1,512);
s = 1-abs(t);
c = cwt(s,1:64,'sym4','abslvl');

## Slide 32: Example 2
Time domain
Time-scale domain

## Slide 33: Discrete Wavelet Transform (DWT)
In order to compute CWT by computers, we need to discretize the continuous time-scale plane
The CWT representation is a very redundant representation
Discretize the continuous time-scale plane on a dyadic (octave) grid: dyadic wavelet transform

## Slide 34: DWT Implementation
G
H
2
2
G
H
2
2
2
2
G
H
+
2
2
G
H
+
x[n]
x[n]
Decomposition
Reconstruction
~
~
~
~
Two-level DWT decomposition
G
H
Half band high pass filter
Half band low pass filter
2
2
Down-sampling
Up-sampling

## Slide 35: DWT Implementation (Contd…)
Length: 512
B: 0 ~ 
g[n]
h[n]
g[n]
h[n]
g[n]
h[n]
2
d1: Level 1 DWT
Coeff.
Length: 256
B: 0 ~ /2 Hz
Length: 256
B: /2 ~  Hz
Length: 128
B: 0 ~  /4 Hz
Length: 128
B: /4 ~ /2 Hz
d2: Level 2 DWT
Coeff.
d3: Level 3 DWT
Coeff.
…a3….
Length: 64
B: 0 ~ /8 Hz
Length: 64
B: /8 ~ /4 Hz
2
2
2
2
2
|H(jw)|
w
/2
-/2
|G(jw)|
w

-
/2
-/2
a2
a1
Level 3 approximation
Coefficients

## Slide 36: DWT in Matlab
[cA, cD]= dwt(S,'wname’)
approximation
signal
name of the wavelet
detail

## Slide 37: Commonly used wavelets

## Slide 38
Low frequency- Approximation
High frequency-Details
Decomposition can be
performed iteratively
DWT decomposition: Approximation and details

## Slide 39
Load signal
Choose wavelet
and number
of levels
Hit Analyze
button
Level 1 coeff.
Highest freq.
Approx. coef.
at level 5
s=a5+d5+…+d1
(Wavedemo_signal)
DWT Implementation (wavemenu in MATLAB)

## Slide 40: Applications of Wavelets
Compression
De-noising
Feature extraction
Discontinuity detection
Data analysis
  Biological data
  Financial data

## Slide 41: Example 1: Compression
DWT is commonly used for compression
Most of the DWT coefficients are insignificant, can be zeroed-out!

## Slide 42: Example 1: Compression (Contd…)

## Slide 43: Example 1: Compression (Contd…)

## Slide 44: Example 2: Compression of ECG Signal

## Slide 45: Example 3: Denoising
(Noisy Doppler)

## Slide 46: Example 4: Discontinuity Detection using DWT
(microdisc.mat)

## Slide 47: Example 5: Discontinuity Detection using CWT
(microdiSsc.mat)

## Slide 48: Wigner-Ville Distribution (WVD)
E. Wigner
He received a Nobel prize in Physics in 1963
He was from Physics background.
Ville was from field of Communications.

## Slide 49: Wigner-Ville Distribution (WVD)
The WVD is a quadratic time–frequency distribution with good resolution in both time and frequency domains.
The WVD of a signal is defined in the time-domain as:
The WVD of a signal is defined in the frequency-domain as:

## Slide 50: Cross Terms in WVD
The WVD of a multicomponent signal
The WVD of a signal is given by
The method based on WVD introduces the cross terms in the time-frequency domain. Problem!

## Slide 51: Example 1
Time domain (sum of two
linear chirp signals with
positive-nagative chirp rates)
Time-frequency domain

## Slide 52: Example 2
Time-frequency domain
Time domain (sum of two
linear chirp signals with
positive-positive chirp rates)

## Slide 53: Example 3
Time-frequency domain
Time domain (sum of two
separated bands of
frequency components)

## Slide 54: Methods for Reduction of Cross Terms
Kernel design
Wavelet decomposition
Perfect reconstruction filter bank
Fourier-Bessel decomposition
Image processing
Cross terms free time-frequency
domain
Matlab codes: Time-frequency toolbox
http://tftb.nongnu.org/

## Slide 55: Hilbert-Huang Transform (HHT)
The HHT is especially suited for analyzing non-linear and non-stationary signals
It has two parts: Empirical mode decomposition (EMD) and Hilbert spectral analysis (HSA)
EMD method provides a set of narrow-band signals known as intrinsic mode functions (IMFs)
The HSA is used to compute the amplitude envelope and instantaneous frequency of the individual IMF

## Slide 56: EMD Method
The EMD method is an adaptive, and data dependent method
The EMD method does not require any condition about the stationary and linearity of the signal
The aim of the EMD method is to decompose the nonlinear and nonstationary signal x(t) into a sum of intrinsic mode functions
Each IMF satisfies two basic conditions:
(i) The complete data set, the number of extrema and the number of zero crossings must be the same or differ at most by one
(ii) The mean value of the envelope defined by the local maxima and local minima is zero

## Slide 57: EMD Method (Contd…)
Step 1: Compute the upper and lower envelopes of the signal x(t) and their mean value m1(t)
Step 2: Compute h1(t)=x(t)-m1(t)
Step 3: Check if h1(t) satisfies the IMF conditions.
Step 4: If not, use h2(t)= h1(t)-m2(t) to obtain new h, where m2(t) is computed from h1(t) as in step 1.
Step 5: Continue until an hk(t) satisfies the IMF conditions. When done, c1(t)=hk(t) is the first IMF.
Step 6: Consider the r(t)=x(t)-c1(t) as the new signal, continue from Step 1 to get the other higher IMFs, upto cN(t).
Process is continued until the residue becomes a monotonous function

## Slide 58
Working Principle of EMD Method: Example
Matlab codes are available at http://perso.ens-lyon.fr/patrick.flandrin/emd.html.

## Slide 59
(Contd…)

## Slide 60
(Contd…)

## Slide 61
(Contd…)

## Slide 62
(Contd…)

## Slide 63
(Contd…)

## Slide 64
(Contd…)

## Slide 65
(Contd…)

## Slide 66
(Contd…)

## Slide 67
(Contd…)

## Slide 68
(Contd…)

## Slide 69
(Contd…)

## Slide 70
(Contd…)

## Slide 71
(Contd…)

## Slide 72
(Contd…)

## Slide 73
(Contd…)

## Slide 74
(Contd…)

## Slide 75
(Contd…)

## Slide 76
(Contd…)

## Slide 77
(Contd…)

## Slide 78
(Contd…)

## Slide 79
(Contd…)

## Slide 80
(Contd…)

## Slide 81
(Contd…)

## Slide 82
(Contd…)

## Slide 83: EMD of healthy EEG signal

## Slide 84: Hilbert Spectral Analysis (HSA)
After decomposition, the actual signal can be represented as a linear combination of narrow-band IMFs (or AM-FM) signals
Amplitude envelope and instantaneous frequency of IMFs are estimated using HSA technique

## Slide 85: Example 1: Synthetic signal

## Slide 86: HHT of synthetic signal

## Slide 87: Conclusion
Time-Frequency representation is a general representation of frequency representation (similarly nonstationary signal is a general representation of stationary signal)
Problems in time-frequency representations:
-Short time Fourier transform (STFT): Selection of type and size of window function
-Wavelet transform (WT): Selection of mother wavelet
-Wigner-Ville distribution (WVD): Presence of cross terms
-Hilbert-Huang transform (HHT): No mathematical representation
Time-frequency analysis is an active area of research

## Slide 88: References
http://users.rowan.edu/~polikar/wavelets/wttutorial.htm
R.B. Pachori and P. Sircar, “A new technique to reduce cross terms in Wigner distribution” Digital Signal Processing, vol. 17, no. 2, pp. 466-474, March 2007.
R. Yan and R.X. Gao, “ Hilbert-Huang transform based vibration signal analysis for machine health monitoring, IEEE Transactions on Instrumentation and Measurement, vol. 55, no. 6, pp. 2320-2329, December 2006.
N.E. Huang, et al., “The empirical mode decomposition and Hilbert spectrum for nonlinear and non-stationary time series analysis”, Proc. Roy. Soc. London A, vol. 454, pp. 903–995, 1998.

## Slide 89: Thank you very much